## Slide 1
Minor project / UG research: progress review
Blind Walking for a Hexapod with Reinforcement Learning:
Terrain Curriculum, Domain Randomisation and Gait Safety
Group member names: [add]
Supervisor: [add]
Date: [add]
Dr. Shyama Prasad Mukherjee
International Institute of Information Technology, Naya Raipur
International Institute of Information Technology, Naya Raipur
Notes: Introduce the project and the team. Say this is a progress review: the walking policy is trained and tested in simulation, and the next step is transfer to the real robot. Fill in names, supervisor and date.

## Slide 2
Content
06/10/26
International Institute of Information Technology, Naya Raipur
2
Introduction
Motivation: Issues and Challenges
Literature Review
Problem definition
Objectives
Proposed Method
Experimental results and discussion
Plan of action for the project
Conclusion and Future Directions
Notes: Walk through the nine sections. The talk is about 15 minutes; the results section is the longest.

## Slide 3
Introduction
06/10/26
International Institute of Information Technology, Naya Raipur
3
Six-legged robot (PhantomX Mark IV): 18 joints driven by Interbotix AX-12A servos
Goal: a learned walking controller that is deployable as is, not tuned by hand
Inputs limited to what the real robot senses: joint angles, joint velocity, IMU, command
Trained in NVIDIA Isaac Lab with reinforcement learning (PPO)
Status: walks with zero falls across terrain and physics variation, in simulation
Notes: The robot is a six-legged PhantomX Mark IV with 18 servo-driven joints. The aim is a controller that uses only its own joint readings and IMU, with no camera and no simulator-only signals. Training is in NVIDIA Isaac Lab with PPO. Be clear that the work is in simulation so far; hardware transfer is next.

## Slide 4
Motivation: Issues and Challenges
06/10/26
International Institute of Information Technology, Naya Raipur
4
Policies that walk well in simulation often fail on the real robot (the sim-to-real gap)
Simulators are too clean: ideal motors, exact friction, no sensing delay or dropped readings
Real servos have limited torque, latency, and missing readings under load
Terrain varies: slopes, stairs, soft ground, changing friction and payload
Reward-based training can hide unsafe motion, e.g. legs passing through each other
Notes: Explain the sim-to-real gap in plain words: a policy that is perfect in a clean simulator often fails on a real robot. Name the three sources: the simulator is too clean, real servos are imperfect, and the terrain varies. Last bullet sets up the problem we solved.

## Slide 5
Literature Review
06/10/26
International Institute of Information Technology, Naya Raipur
5
Approach | How it works | Limitation for our goal
Hand-designed gait generators | Fixed rhythmic leg patterns | Manual tuning; weak on unseen terrain
RL on flat ground (PPO) | Learns walking from a reward | Brittle off flat ground; uses simulator-only signals
RL + terrain curriculum + domain randomisation | Harder terrain over time; randomised physics | Costly training; needs realistic parameter ranges
Vision-guided foothold planning | Camera sees obstacles and plans footholds ahead | Needs camera, depth sensing and more compute
[Add 5–8 cited papers per approach, with reference numbers]
Notes: Group the literature into four approaches, not paper by paper. Explain where each falls short for a blind, deployable walker. Replace the placeholder with the cited papers before presenting; the notes file lists what to add.

## Slide 6
Problem Definition
06/10/26
International Institute of Information Technology, Naya Raipur
6
Learn a walking controller for a six-legged robot that uses only what the real robot can sense, stays upright on varied terrain, and transfers to hardware without retuning.
Sensing: joint angles and velocity from noisy, sometimes dropped readings; IMU; no ground truth
Terrain: flat ground, stairs up to 4 cm, slopes up to about 20°, soft and slippery ground
Safety: no falls and no leg-to-leg collisions
Notes: This is the problem in one sentence, then the three constraints. Stress that the robot must not see anything the real robot cannot sense. The three bullets map to the next sections.

## Slide 7
Research Gap
06/10/26
International Institute of Information Technology, Naya Raipur
7
1
Brittle off flat ground
Flat-ground policies are rarely tested with realistic servo limits and missing sensor readings.
2
Simulator-only signals
Standard setups give the policy ground-truth velocity and exact joint velocity, which a real robot does not have.
3
Unsafe gaits go unseen
Stride and speed metrics can look good while legs pass through each other. Geometric checks are needed.
Notes: Three gaps, each tied to a result later. Gap 1 motivates the servo model and terrain curriculum. Gap 2 motivates removing ground-truth velocity. Gap 3 is the problem we fixed, covered in detail later.

## Slide 8
Objectives
06/10/26
International Institute of Information Technology, Naya Raipur
8
Build a deployable blind walking policy that uses only signals the real robot has
Make it robust: terrain curriculum (flat to stairs and slopes) and domain randomisation
Make the gait physically safe: legs clear each other and land at a sensible reach
Evaluate reproducibly: held-out terrain, fixed seeds, results across five training seeds
Notes: Four objectives, matching the constraints. The fourth is about how we report results: fixed seeds, held-out terrain and several training seeds, so the numbers can be reproduced.

## Slide 9
Proposed Method: Control Loop
06/10/26
International Institute of Information Technology, Naya Raipur
9
Speed and turn command
Gait clock (six legs)
Policy
(PPO actor network)
18 joint
position targets
Servo model + robot
(AX-12A limits, dropped reads, latency)
Sensors: joint angle and
velocity, IMU, last action
Reward and critic:
training only
Only signals the real robot has reach the policy: no ground-truth velocity, no simulator-only contact data.
Notes: Read the diagram left to right. The command and gait clock go into the policy. The policy outputs 18 joint targets. The servo model and the robot respond, and the sensor readings feed back. The reward and critic exist only in training and are not on the robot.

## Slide 10
How We Built the Policy: Four Stages
06/10/26
International Institute of Information Technology, Naya Raipur
10
1. Correct the simulator
Foot contact point fixed
Friction and leg order checked
Gait clock fixed
2. Realistic servos (S0a)
AX-12A servo model
Missing readings simulated
No ground-truth velocity
3. Commands and terrain (S0b)
Speed and turn commands
Terrain curriculum (levels 0–14)
Full domain randomisation
4. Blind terrain policy (S1)
Surface patches with changing friction
Learned velocity estimate
Five training seeds
Each stage is gated: zero falls, speed tracking within 10 %, and no unsafe leg contact.
Notes: Each stage adds one thing and must pass its gate before the next starts. Stress the order: the simulator is corrected first, then the servos, then commands and terrain, then the spatial material patches.

## Slide 11
Training Terrain and Domain Randomisation
06/10/26
International Institute of Information Technology, Naya Raipur
11
Randomised quantity | Training range
Foot friction (static) | 0.3 – 1.1
Ground compliance | 50 % of envs soft
Payload on the body | 0.1 – 1.0 kg
Servo stall torque | × 0.9 – 1.1
Servo backlash | 0.3° – 1.0°
Command latency | 5 – 10 ms
IMU bias per episode | σ 0.05 m/s², 0.01 rad/s
Terrain (training) | Levels 0–14: flat to 4 cm stairs, slopes
Surface patches (S1) | 10 surface types, 0–0.8 m blends
Why this helps transfer
Policy must work across the whole range, not one tuned setting
Held-out terrain (levels 15–20) is used only for testing
Ranges are provisional until the bench measurements are done
Notes: This is the main sim-to-real slide. Each range brackets something the real robot may differ on: friction, payload, servo strength, delay and sensor noise. The held-out levels 15–20 are never used in training. Be honest that the ranges are provisional until the robot is measured on the bench.

## Slide 12
Problem We Solved: Legs Passing Through Each Other
06/10/26
International Institute of Information Technology, Naya Raipur
12
Symptom: an earlier policy's legs passed through each other (worst gap −6.3 cm)
Root cause: self-collision was off in simulation, so nothing penalised leg contact
Why it was missed: speed and stride looked good; only a geometric probe showed it
Chart: Worst leg-to-leg gap (cm): positive = clear gap
| Earlier policy | Gait-corrected policy | Final S1 (5-seed mean)
Worst leg-to-leg gap (cm) | -6.3 | 1.3 | 0.9
Notes: The problem: an earlier policy's legs overlapped in simulation, with the worst gap at minus 6.3 cm, and about 22 % of steps were under the 2 cm safety margin. The root cause is that self-collision was off, so nothing penalised it. The chart shows the gap after the fix: positive means a clear gap.

## Slide 13
Problem We Solved: The Fix
06/10/26
International Institute of Information Technology, Naya Raipur
13
Leg-proximity penalty
2 cm safety margin between leg shapes. Cheap to satisfy, far below the speed reward.
Coordinated swing
Middle and back legs lift together and land at the rest reach, not a tucked fold.
Retrain from scratch
Corrected reward, no warm start: 12,214 iterations instead of 20,749 (0.59×).
Measure | Before | After
Worst leg gap | −6.3 cm | +1.3 cm
Toe path per swing | ≈ 20 cm | 5.7–7.9 cm
Landing vs lift-off | 5.5 cm inside | ≈ 1 cm outside
Result: no leg overlap, and speed and turn tracking are kept (both within the gates).
Notes: Three changes: a leg-proximity penalty with a 2 cm margin, coordinated swing so the middle and back legs lift together and land at the rest reach, and retraining from scratch. The economics check: walking still beats standing and falling. The lesson for the audience: stride metrics alone do not catch unsafe gaits.

## Slide 14
Results: Training-Range Gates (Stage S0b)
06/10/26
International Institute of Information Technology, Naya Raipur
14
Measure | Result | Gate
Falls | 0 in 17,408 episodes | 0
Stride error, 0.10 m/s | +1.0 / +0.3 / −0.7 % | ±10 %
Stride error, 0.15 m/s | −0.2 / −0.6 / −1.4 % | ±10 %
Turn on the spot (±0.3 rad/s) | +0.32 / −0.31 | ±0.3
Standing foot contact | 97 % | report
Terrain levels 0–14 | 108 of 108 cells pass | all pass
Held-out levels 15–20 | 50 of 72 cells, 0 falls | report
Chart: Stride error (%) by terrain level
| Level 0 | Level 5 | Level 9
0.10 m/s | 1 | 0.3 | -0.7
0.15 m/s | -0.2 | -0.6 | -1.4
Notes: Zero falls in 17,408 evaluation episodes. Stride error is within plus or minus 1.4 % at both speeds, and turning is close to the commanded 0.3 rad/s in both directions. All 108 training terrain cells pass. On the held-out levels 15–20, 50 of 72 cells pass, with no falls; be open that these harder cells are weaker.

## Slide 15
Results: Blind Terrain Policy (Stage S1, Five Seeds)
06/10/26
International Institute of Information Technology, Naya Raipur
15
Measure (mean ± sd over 5 seeds) | Result
Falls | 0 in 21,760 episodes
Stride error, 0.10 / 0.15 m/s | +1.2 ± 1.1 % / −1.8 ± 1.1 %
Turn on the spot (±0.3 rad/s) | +0.302 / −0.301
Worst leg-to-leg gap | +0.9 ± 0.4 cm (all seeds positive)
Front foot lift | 4.4 ± 0.2 cm
Velocity error: rigid / slippery | 0.028 / 0.056 m/s
Standing foot contact | 0.92 ± 0.01
Chart: Per-seed stride error (%)
| Seed 42 | Seed 43 | Seed 44 | Seed 45 | Seed 46
Stride error at 0.10 m/s (%) | 0.5 | 0.3 | 2.9 | 0.7 | 1.7
Stride error at 0.15 m/s (%) | -2.6 | -2.6 | 0.1 | -2.3 | -1.6
Notes: Five training seeds, all passing. Falls are zero in 21,760 episodes. The per-seed chart shows the spread: the difference between seeds is small compared with the gate margins. The velocity error is about 0.03 m/s on rigid ground and about 0.06 m/s on slippery ground. This is the policy that goes forward to hardware.

## Slide 16
Plan of Action for the Project
06/10/26
International Institute of Information Technology, Naya Raipur
16
Done
Simulator corrected (contact point, friction, clock)
Realistic servo model; no ground-truth velocity
Gait and terrain policy: zero falls in simulation
Blind terrain policy: five seeds, zero falls
Next
Headroom test: blind policy vs. one given foresight. Pre-set go/no-go for camera work
Bench measurements (servo gains, latency, drop rate, foot friction); update the ranges
If the test passes: camera-based foothold prediction (depth, then RGB-D)
Zero-shot transfer to the PhantomX, with safety limits on joint angles
Phase 3 (design stage): a visuo-proprioceptive model, compared under the same protocol.
Notes: Left is done. Right is the plan. Be clear that the headroom test is the decision point: it decides whether the camera-based stages go ahead. Phase 3 is only mentioned here, as a design-stage model that will be compared under the same protocol.

## Slide 17
Conclusion and Future Directions
06/10/26
International Institute of Information Technology, Naya Raipur
17
A blind walking policy passes every gate with zero falls, across five training seeds
Leg collisions were found with a geometric check, not the speed metric; the fix is in the reward
Terrain and randomisation ranges are the bridge to the real robot
Future directions
Hardware transfer on the PhantomX, with bench-calibrated randomisation
Camera-based foothold prediction, if the headroom test justifies it
Notes: Close on three points: a blind walker that passes every gate across five seeds, a gait fix that came from a physical check rather than the speed metric, and the next steps. Stop before the headroom result, which is not part of this review.

## Slide 18
Thank You
Questions and feedback welcome
Group member names: [add]
Supervisor: [add]
Date: [add]
Dr. Shyama Prasad Mukherjee
International Institute of Information Technology, Naya Raipur
International Institute of Information Technology, Naya Raipur
Notes: Thank the panel and open for questions.